## Slide 1: Progress Report
Hiroo Miyata
2022/08/12

## Slide 2: Table of Contents
(Repeat) Preprocessing of EMG signals
Visualization of EMG signals around Go Cue
Future Direction

## Slide 3: Remove baseline noise by Notch filter
(Butterworth, second order, cutoff frequency= Hz (n=1,…,8))
Time (second)
Voltage(a.u)
Removing baseline noise make signal more clear
PSD spectrum shows only baseline noise is removed
Raw Signal

## Slide 4: ECG signal wasn’t removed by bandpass filter
EMG signal at rest(100~110s) at different cutoff-frequency bandpass filter
Cut-off frequency as proposed is around 30 Hz (Surface Electromyography Signal Processing and Application: A Review 2009)
10 Hz
30 Hz
40 Hz
50 Hz
50 Hz

## Slide 5: Remove ECG by adaptive filter
Adaptive filter using least square fit
(A.L. Hof, Journal of Electromyography and Kinesiology, 2009)
H(t)
emg(t)
ecg(t)
ecg’(t)
H(t)の求め方の説明
Least square fitの説明
new emg(t)
Before
Detected
After

## Slide 6: Remove unrelated signal by bandpass filter
(Butterworth, second order, cutoff frequency= ~20 Hz and 450 Hz ~
Motion artifact is 0 ~ 20 Hz (Anghoon, Biomedical Signal Processing, 2019)
PSD spectrum proves it correctly removes signals
In irrelevant frequency bands
Time (second)
Voltage(a.u)
Raw Signal

## Slide 7: Rectify and smooth signal
Rectification: negative value to positive
Smoothing: Moving Average or Root Mean Square
The EMG signal is smoothed
Time (second)
Voltage(a.u)
Smoothed by 50ms time window
Time (second)
Voltage(a.u)
Smoothed by 200ms time window

## Slide 8: Table of Contents
(Repeat) Preprocessing of EMG signals
Visualization of EMG signals around Go Cue
Future Direction

## Slide 9: Visualization of EMG around Go Cue
Hypothesis
EMG signal and reach direction have a relationship during motion
EMG and reward have a relationship at delay period

## Slide 10: Relationship between EMG and direction
Methods
Use only succeeded trial EMG
Use EMG data around Go Cue (-200ms ~ +600ms)
Gray lines are each trials and black line is a mean value of all trial
Position of figure means direction

## Slide 11: Relationship between EMG and direction
Methods
Use only succeeded trial EMG
Use EMG data around Go Cue (-200ms ~ +600ms)
Gray lines are each trials and black line is a mean value of all trial
Position of figure means direction

## Slide 12: Relationship between EMG and direction
Methods
Use only succeeded trial EMG
Use EMG data around Go Cue (-200ms ~ +600ms)
Gray lines are each trials and black line is a mean value of all trial
Position of figure means direction

## Slide 13: Relationship between EMG and direction
Methods
Use only succeeded trial EMG
Use EMG data around Go Cue (-200ms ~ +600ms)
Gray lines are each trials and black line is a mean value of all trial
Position of figure means direction

## Slide 14: Visualization of EMG around Go Cue
Hypothesis
EMG signal and reach direction have a relationship during motion
  Upper directions increase EMG
  Lower directions decrease EMG
EMG and reward have a relationship at delay period

## Slide 15: Relationship between EMG and direction
Methods
Use only succeeded trial EMG
Use EMG data around Go Cue (-200ms ~ +600ms)
Gray lines are each trials and black line is a mean value of all trial
Position of figure means direction

## Slide 16: Relationship between EMG and direction
Methods
Use only succeeded trial EMG
Use EMG data around Go Cue (-200ms ~ +600ms)
Gray lines are each trials and black line is a mean value of all trial
Position of figure means direction

## Slide 17: Relationship between EMG and direction
Methods
Use only succeeded trial EMG
Use EMG data around Go Cue (-200ms ~ +600ms)
Gray lines are each trials and black line is a mean value of all trial
Position of figure means direction

## Slide 18: Visualization of EMG around Go Cue
Hypothesis
EMG signal and reach direction have a relationship during motion
  Upper directions increase EMG
  Lower directions decrease EMG
EMG and reward have a relationship at delay period

## Slide 19: Table of Contents
Modification of Preprocessing of EMG signals
Visualization of EMG signals around Go Cue
Future Direction

## Slide 20: What I’ll do
Continue EMG preprocessing?
Participate in focus task research?

## Slide 21: Relationship between EMG and direction
Methods
Use only succeeded trial EMG
Use EMG data around Go Cue (-200ms ~ +600ms)
Gray lines are each trials and black line is a mean value of all trial
Position of figure means direction

## Slide 22: Check : the raw signals before preprocess
Time (second)
Voltage(mV)
Time (second)
Voltage(mV)
Noise level depends on the muscle area.
(Also varies from day to day)
Raw Signal
Raw Signal
Notes: Best Caseの信号と最悪の信号を見せる